## Slide 1: TC2: B mode brain sonography
Brain Parenchyma Imaging Basis and Protocol
Aleksandra M. Pavlovic, Assist. Prof.
University of Belgrade, Faculty for Special Education and Rehabilitation

## Slide 2: Faculty Disclosure
Company Name | Honoraria/ Expenses | Consulting/ Advisory Board | Funded Research | Royalties/ Patent | Stock Options | Ownership/ Equity Position | Employee | Other (please specify)
Example: company XYZ |  |  |  |  |  |  |  | 
x | No, nothing to disclose
 | Yes, please specify:

## Slide 3
Transcranial B mode sonography (TCS) is a neuroimaging technique that displays the brain parenchyma and the intracranial ventricular system through the intact skull
The first report on TCS: Becker et al, 1995, reported increased echogenicity of substantia nigra (SN) in patients with Parkinson’s disease
No disease-specific abnormality had been routinely shown by other structural neuroimaging methods before this finding
Present-day TCS systems can achieve a higher image resolution compared to MR
In-plane image resolution of intracranial structure in the focal zone is app. 0.7 x 1.1 mm (compared to MR under clinical conditions, app. 1.0 X 1.0 mm).
Brain Parenchyma Imaging Basis
https://n.neurology.org/content/45/1/182

## Slide 4
An optimal TCS examination requires a high-end ultrasound machine with a 2-4 (3.5) MHz phased-array sector transducer (also used for transcranial duplex sonography)
The best visualization of the brain parenchyma in adults is achieved with:
  imaging depth set to 14-15 cm
  dynamic range between 40-60 (45-55) dB
  image brightness: adjust as needed (or “tissue optimization” if available)
  Time Gain Compensation: adjust as needed (or “tissue optimization” if available)
  With these settings the best resolution is achieved in a distance of 5-9 cm from the probe – the focal zone; additionally, the focus can be manually adjusted on the screen to increase the local resolution of the structures
Equipment and Settings

## Slide 5
Ultrasound examination should be performed in a darkened room
The examiner usually sits behind the head of the patient who lies in supine position
The investigation is performed through the transtemporal bone window consecutively from each side
The transducer is placed on the temporal bone in front of the upper part of the auricle parallel to the orbitomeatal line (passes through the outer canthus of the eye and the center of the external auditory meatus)
The transducer is carefully moved back and forth in order to find the best imaging window
Axial images of the brain stem, basal ganglia, and ventricles are obtained
Equipment and Settings
https://radiologykey.com/transcranial-ultrasonography-in-movement-disorders/
https://www.e-jmd.org/journal/view.php?number=101

## Slide 6
In 10-15% Caucasian population, particularly in elderly females (up to 25%), also in Asians, the examination may be unsuccessful/partially successful due to an inadequate bone window
Bone window: the main limitation
▶ Quality criterion of good image quality:
The contralateral skull bone is clearly visualized over its whole extension in the imaging sector.
Walter U, Školoudík D. Ultraschall Med 2014

## Slide 7
Hyper-echogenic
The planimetrically measured area of the echogenic signal within a defined brain area is larger in the patient than in the general population (e.g. SN)
The visually rated intensity of the ultrasound signal is increased compared with the surrounding brain tissue
Hyperechogenic or Hypoechogenic?
Hypo-echogenic
The planimetrically measured echogenic area is smaller in the patient than in the general population (e.g. SN)
A structure that has an echogenicity that is usually high (e.g. BR) is shown to have a low echogenicity, with discontinuity or invisibility of the echosignal
Normal SN
Hyperechogenic SN
Hypoechogenic SN

## Slide 8
Scanning Protocol: Standard Planes
Two standard transtemporal axial scanning planes, defined by cerebral landmark structures are used:
Mesencephalic plane
Third Ventricle plane
Berg, Godau, Walter. Lancet Neurology 2008

## Slide 9
Scanning Protocol: Standard Planes
Two standard transtemporal axial scanning planes, defined by cerebral landmark structures are used:
Mesencephalic plane
Third Ventricle plane
Berg, Godau, Walter. Lancet Neurology 2008

## Slide 10
Scanning Protocol: Mesencephalic Plane
Berg, Godau, Walter. Lancet Neurology 2008
Berg, Godau, Walter. Lancet Neurology 2008
Walter. Perspectives in Medicine 2012
Ylmaz, Berg, Int R Neurobiol 2018
Midbrain appears hypoechogenic (dark) surrounded by the hyperechogenic (bright) basal cisterns
Structures to be visualized:
SN
brainstem raphe (BR)
nucleus ruber (NR)
Transducer is at the orbitomeatal line
Medially located butterfly shaped mesencephalon (midbrain) at app. 7 cm penetration depth

## Slide 11
Scanning Protocol: Mesencephalic Plane, SN
Berg, Godau, Walter. Lancet Neurology 2008
Ylmaz, Berg, Int R Neurobiol 2018
SN visualization
Hyperechogenic structure caudal of the pedunculus cerebri
SN is assessed on the ipsilateral side of the transducer within the hypoechogenic mesencephalon
Since the SN is a rather small structure, the transducer is carefully moved back and forth in order to find the image in which the SN is displayed at its largest size
Becker et al, Neurology 1995

## Slide 12
Scanning Protocol: Mesencephalic Plane, SN
Ylmaz, Berg, Int R Neurobiol, 2018
SN measurements
After freezing and magnifying the image two to threefold, planimetric measurement is performed by encircling the area of the SN manually using the area measurement function of the machine
Image A: a healthy individual, SN area is 0.12cm2
Normal finding
Image B: Parkinson's disease (PD), SN area is 0.39cm2
SN hyperechogenicity, SN+
SN cut-off values
Should be calculated by taking the 90th percentile of SN values of at least 50 healthy individuals > 50 years
Some studies/centers use additionally the 75th percentile as a cut-off value for detection of a “moderate SN+”

## Slide 13
Scanning Protocol: Mesencephalic Plane, SN
SN cut-off values
May vary according to the ultrasound machine and the population assessed
Usually, if ≥0.19 (0.20) cm2 = hyperechogenic SN
If the sum of both SN is < 1 SD of the mean of the general population (<0.21 cm2) = hypoechogenic SN
Potential drawbacks
Planimetric measurement is taking two-dimensional size of the SN into account
Not to be included into the area measurements of the SN
Penetrating arteries (hyperechogenic)
Basal cisterns (reverberating echoes)
Echosignals of the red nucleus (although usually does not relevantly interfere with SN measurement)
Walter U, Školoudík D. Ultraschall Med 2014

## Slide 14
Scanning Protocol: Mesencephalic Plane, BR
Berg, Godau, Walter. Lancet Neurology 2008
Ylmaz, Berg, Int R Neurobiol 2018
Brainstem Raphe (BR) visualization
In healthy individuals, the mesencephalic part of the midline raphe is visualized as a continuous hyperechogenic line located in the middle of the mesencephalon
BR should be assessed regarding its continuity
BR ehogenicity should be classified as reduces only if examination from both sides shows reduced echosignal under adequate imaging conditions
An interruption or the absence of the hyperechogenic line is abnormal and has been related to depression
Becker et al, Neurology 1995

## Slide 15
Scanning Protocol: Mesencephalic Plane, red nucleus
Nc. ruber (NR) visualization
It is located in the caudal midbrain, between the raphe and SN, typically seen as a small white dot or two small stripe-like echosignals at its medial and lateral border, respectively (orange arrowhead)
Sometimes its lateral echosignal cannot be discriminated from the echosignals of the SN
Hyperechogenicity of the NR is shown when either the area of the echogenicity is extended or if NR seems to be more echogenic than the basal cisterns
Walter U, Školoudík D. Ultraschall Med 2014

## Slide 16
Scanning Protocol: Standard Planes
Two standard transtemporal axial scanning planes, defined by cerebral landmark structures are used:
Mesencephalic plane
Third Ventricle plane
Berg, Godau, Walter. Lancet Neurology 2008

## Slide 17
Scanning Protocol: Standard Planes
Two standard transtemporal axial scanning planes, defined by cerebral landmark structures are used:
Mesencephalic plane
Third Ventricle plane
Berg, Godau, Walter. Lancet Neurology 2008

## Slide 18
Scanning Protocol: Third Ventricle Plane
The third ventricle plane is located rostral of the mesencephalic plane
This plane is reached by tilting the probe 10-25 degrees upward from the axially scanned mesencephalic plane
Structures to be visualized:
third ventricle
lateral ventricles
thalami (T)
basal ganglia: caudate nucleus (CN), lentiform nucleus (LN)
Blue arrow head – calcified pineal gl.
Small white arrow – III ventricle
Long white arrow – anterior horn of the lateral ventricle
Ylmaz, Berg, Int R Neurobiol, 2018

## Slide 19
Scanning Protocol: Third Ventricle Plane
At the beginning of the examination, the pineal gland (blue arrow head) can be spotted in the middle of the imaging plane as a round calcified structure which can be used as a landmark
In front of the pineal gland, the ependyma of the third ventricle appears as two parallel hyperechogenic lines (small white arrow)
On both sides of the third ventricle hypoechogenic egg-shaped thalami can be seen
Further to anterior, the frontal horn of the lateral ventricle (long white arrow) can be seen on the contralateral side
Both the III ventricle and the frontal horn of the contralateral ventricle are assessed by drawing a perpendicular line between the ventricle borders (between the inner layers of the ependyma)
Ylmaz, Berg, Int R Neurobiol, 2018

## Slide 20
Scanning Protocol: Third Ventricle
The cut-off values of the III ventricle are < 7/10 mm for individuals younger or older than 60 years
The cut-off values of the frontal horn are < 17/20 mm for individuals younger or older than 60 years
Bouwmans et al. Int R Neurobiol 2018
Normal III ventricle
Enlarged III ventricle

## Slide 21
Scanning Protocol: Basal Ganglia
Adjacent to the frontal horn, the CN is located, which is also visualized from the contralateral side
Between the CN and T, the LN is located, hardly seen in healthy individuals due to its isoechogenicity with the surrounding tissue
The basal ganglia and the T are assessed on a contralateral side, in a semi-quantitative way
Generally, these structures are isoechogenic to the surrounding brain parenchyma
Walter U, Školoudík D. Ultraschall Med 2014

## Slide 22
Scanning Protocol: Basal Ganglia
These structures are considered hyperechogenic if more bright compared to surrounding white matter or when compared to calcified structures (pineal gland, choroid plexus, skull)
The size of the echogenic areas of the structure can be measured
Berg, Godau, Walter. Lancet Neurology 2008
Image C. Dot-like hyperechogenicity of the medial part of the lenticular nucleus (L) (arrow). Seen in idiopathic dystonia, atypical Parkinson’s syndrome, Wilson’s disease.
Image D. Extensive hyperechogenicity of the lenticular nucleus (L) (arrow). Seen in Wilson’s disease.

## Slide 23
Scanning Protocol: Other planes
Although not widely used, there are other imaging planes providing additional information:
Cella media plane (3): tilting the probe further upward from the third ventricle plane (2), scanning angle of 25-30 degrees; the middle part of the contralateral lateral ventricle can be measured
Cerebellar plane: reached from the mesencephalic plane (1) by turning the top edge of the probe app. 45 degrees posterior in order to visualize the vermis
Coronal plane: turning the probe 90 degrees posterior to visualize the brainstem, SN, ventricles, basal ganglia on the ipsilateral side and medial temporal lobe
https://www.e-jmd.org/journal/view.php?number=101

## Slide 24
Quality criterion of adequate standard of TCS report
„The report includes
the rating (normal vs. abnormal) and, if obtained, the quantitative measures of echogenicity of SN, red nucleus, midbrain raphe, lenticular nucleus, caudate nucleus (and of other brain structures if investigated)
as well as the widths of the 3rd ventricle and frontal horns of lateral ventricles (and of other brain structures if investigated)
as well as the final interpretation of TCS findings in response to the diagnostic question.“
Walter, Školoudik. Ultraschall in Med 2014

## Slide 25
The main limitation of the TCS is the lack of bone window
The success of the examination is highly dependent on the examiner and their expertise/experience
Limitations of the TCS
Advances of the TCS
Different visualization of brain structures compared to other neuroimaging methods due to different physical imaging principle
High resolution image of deep and small structures
Safe/harmless, time and cost-efficient, patient-friendly and widely-available imaging tool
Quick to do in patient with moving disorders or less cooperative
Expanding indications (acute stroke, neurocritical care, deep-brain stimulation, medial temporal lobe assessment)

## Slide 26
Recommended reading
Yilmaz R, Berg D. Transcranial B-Mode Sonography in Movement Disorders. Int Rev Neurobiol 2018;143:179-212.
Walter U, Školoudík D. Transcranial sonography (TCS) of brain parenchyma in movement disorders: quality standards, diagnostic applications and novel technologies. Ultraschall Med 2014;35(4):322-31.
Berg D, Walter U (eds). Transcranial Sonography of Movement Disorders. Int Rev Neurobiol, 2010: 90.
Berg D, Godau J, Walter U. Transcranial sonography in movement disorders. Lancet Neurol 2008; 7:1044–1055.
*Walter U, Behnke S, Eyding J, et al. Transcranial brain parenchyma sonography in movement disorders: state of the art. Ultrasound Med Biol 2007;33:15–25.
*Consensus guidelines on TCS use in movement disorders

## Slide 27
Thank you for your attention!