## Slide 1
For Research & Investigational Use Only. Not for Commercial Use.
Comparison Of Transcranial Doppler Signal To Noise In Human And Robotically Acquired Clinical Control Groups
Samuel G. Thorpe1 │ Corey M. Thibeault1 │ Kian Jalaleddini1 │ Nicolas Canac1 │ Amber Y. Dorn1 │Thomas Devlin2 │ Robert Hamilton1
1 NovaSignal, Corp. Los Angeles, CA. 2 Erlanger Neuroscience Institute. Chattanooga, TN
High training requirements for ultrasound technicians have long been an obstacle to widespread adoption of TCD for acute stroke assessment, despite its status as a noninvasive, inexpensive, and conveniently portable imaging technology.
Collection and assessment of TCD exam signal quality is dependent upon the expertise of the person performing the exam, introducing a level of subjectivity that may vary across users and amount of experience.
Introduction
Purpose
In this work we compare TCD signal quality measured by an expert human sonographer to that acquired robotically with NovaGuide, a device which automates TCD data acquisition, in a clinical control population.
Methods
Patient Population and Data Collection
Statistical Analysis
We express the power of the residuals in terms of Signal to Noise Ratio (SNR):
Where P is the power defined as the sum of the squared samples of a signal:
results
Figure 2. Distribution of SNR observed for NovaGuide and handheld TCD recordings.
results
Figure 3. Distribution of rejected beats for NovaGuide and handheld TCD recordings.
Notably, the proportion of rejected signal averaged 12% (SD=9%) for NovaGuide recordings, compared to 14% (SD=10%) for manual recordings, with observed group differences exceeding threshold significance (p<0.01).
conclusions
These preliminary results suggest NovaGuide is capable of measuring TCD in a clinical setting with signal quality which does not significantly deviate from an expert human sonographer, and includes a smaller proportion of signal rejected as artifact.
These results demonstrate the utility of NovaGuide in the clinical setting as an automated, expert-equivalent TCD tool.
Questions?
Any questions can be directed to Robert Hamilton, Ph.D. (robert@novasignal.com)
Methods
Figure 1. The NovaGuide Intelligent Ultrasound System, used to insonate the MCA in all subjects.
Subjects were enrolled at Erlanger Medical Center (Chattanooga, TN, USA), as part of an ongoing TCD study of large vessel occlusion (LVO).
To ensure that the presence of LVO did not impact signal quality, only CTA-confirmed non-LVO control subjects were included in the current analysis.
CBFV waveforms were recorded in 30 second intervals at multiple depths along the left/right Middle Cerebral Arteries of 105 total subjects: 71 via NovaGuide, and 34 via manual examination by the same expert sonographer
To assess signal quality for each recording, both SNR, and the proportion of each recording rejected as artifact, were computed and subsequently compared across groups via bootstrapped empirical p-values, with a critical level of 0.05 specified for significance.
NovaGuide
An average SNR of 10.57 (SD=4.23) was observed for NovaGuide exam recordings, compared to an average of 10.29 (SD=4.68) observed for manual recordings.
Observed group differences (p=0.086) did not reach the threshold for significance.
NovaGuide
Selected References
1. Jalaleddini K, Thorpe S, Canac N, bioRxiv AD-, 2019 undefined. Method for Modeling Residual Variance in Biomedical Signals Applied to Transcranial Doppler Ultrasonography Waveforms. biorxiv.org.